## Slide 1
REVIEW #1
Real-Time PPE Compliance Monitoring System
Automated Safety Surveillance for Industrial & Construction Sites
Architecture, Model & Data Pipeline
Objective: Develop an automated, real-time computer vision system to monitor Personal Protective Equipment (PPE) compliance, mitigate workplace accidents, and maintain strict industrial safety standards.
Core Functionality: Automatic detection of safety gear violations (hard hats, masks, safety vests) alongside machinery and personnel tracking across live camera feeds and recorded videos.
Review Focus Areas:
Construction Site Safety Dataset & Class Distribution
YOLOv8 Computer Vision Architecture & Training
End-to-End System & API Architecture
Complete Technology Stack
Expected Analytical Outputs & Incident Logging

## Slide 2
Project Overview & Problem Statement
Mitigating Industrial Hazards through Computer Vision
The Industrial Challenge
Construction and manufacturing zones face high occupational hazards and safety non-compliance.
Manual safety inspection is labour-intensive, error-prone, inconsistent, and cannot provide continuous 24/7 coverage.
Proposed Solution
Real-time automated visual inspection pipeline using state-of-the-art object detection.
Instantaneous identification of compliant vs. non-compliant personnel.
Automated generation of violation logs with timestamped visual evidence.
Key Monitored Classes
Compliance Classes
Hardhat, Mask, Safety Vest
Violation Classes
NO-Hardhat, NO-Mask, NO-Safety Vest
Contextual & Neutral Classes
Person, Machinery, Vehicle, Safety Cone

## Slide 3
Dataset Characteristics & Class Distribution
Construction Site Safety Dataset (Kaggle)
Dataset Source & Link
Kaggle URL: https://www.kaggle.com/datasets/snehilsanyal/construction-site-safety-image-dataset-roboflow
Origin: Construction Site Safety Image Dataset (Roboflow Universe via Kaggle)
Dataset Scale & Partition
Total Images: 2,801 annotated images
Total Annotations: 38,352 object bounding boxes
Training Split: 2,240 images (30,684 annotations, ~80%)
Validation Split: 280 images (3,554 annotations, ~10%)
Test Split: 281 images (4,114 annotations, ~10%)
Class Annotation Breakdown
Person: 9,872 instances (primary contextual object)
Machinery & Vehicles: 5,346 machinery and 1,628 vehicle instances
Safety Equipment: 4,158 NO-Safety Vest, 3,502 Safety Cone, 3,334 Hardhat, 3,250 NO-Mask, 3,135 Safety Vest, 2,427 NO-Hardhat, 1,700 Mask
Dataset Relevance
High diversity of angles, lighting conditions, occlusions, and multi-worker density typical of live industrial sites.

## Slide 4
Data Augmentation & Preprocessing Pipeline
Robustness Engineering for Dynamic Industrial Environments
Input Preprocessing
Spatial Standardisation: 640 x 640 pixel resolution (BCHW tensor format)
Normalisation: Pixel values scaled to [0.0, 1.0] range
Data Augmentation Strategy
Photometric Distortions: HSV colour jittering (Hue: 0.015, Saturation: 0.7, Value/Brightness: 0.4) for varying daylight conditions
Geometric Transformations: Rotation (+-5.0 degrees), Translation (+-0.1), Scaling (+-50%), Shear (+-2.0 degrees), Horizontal Flip (p = 0.5)
Advanced Composition: Mosaic Augmentation (scale 1.0) and Mixup (0.1) to boost detection of small and partially occluded safety gear
Regularisation: Copy-Paste augmentation (0.1) and disabling Mosaic in the final 10 epochs for fine-grained boundary stabilisation

## Slide 5
Computer Vision Model Architecture
YOLOv8m (Ultralytics) Single-Stage Object Detector
Model Selection: YOLOv8m (Medium): Balances high inference accuracy (mAP) with real-time frame rates (>40 FPS).
Backbone
Modified CSPDarknet53 with C2f (Cross-Stage Partial with 2 Convolutions) modules for rich multi-scale feature extraction.
Neck
Path Aggregation Network (PANet) and Feature Pyramid Network (FPN) for seamless multi-scale contextual semantic fusion.
Detection Head
Anchor-free, decoupled head separating classification and bounding box regression branches to accelerate convergence.
Loss Functions
Complete IoU (CIoU) and Distribution Focal Loss (DFL) for precise bounding box localisation. Binary Cross-Entropy (BCE) with Label Smoothing (0.1) for class classification.

## Slide 6
Model Training, Hardware & Performance Metrics
Rigorous Training Pipeline & Quantitative Evaluation
Training Infrastructure
Hardware: Dual NVIDIA Tesla T4 GPUs (16 GB VRAM each)
Framework: PyTorch 2.10.0, CUDA 13.0, Ultralytics 8.4.30
Optimization: SGD (momentum: 0.937, weight decay: 0.0005) with Cosine Annealing Learning Rate Schedule (Initial LR: 0.01, Final LR: 0.0001)
Training Duration: 100 Epochs (Best model achieved at Epoch 88)
Quantitative Results (Test Set Evaluation)
Overall Performance: mAP@0.5 = 0.8807 (88.07%), mAP@0.5:0.95 = 0.6425
Precision & Recall: Precision = 92.27%, Recall = 80.92%
Critical Class Accuracies (AP@0.5): Machinery (96.40%), Mask (95.48%), Person (93.38%), Vehicle (90.57%), NO-Safety Vest (89.17%), NO-Hardhat (87.62%), Safety Vest (85.05%), NO-Mask (82.98%), Hardhat (82.76%)
Inference Speed: 23.5 ms per frame (42 FPS), fully supporting real-time streaming

## Slide 7
System Architecture & Workflow Pipeline
Client-Server Decoupled Architecture with Asynchronous Inference
End-to-End Operational Pipeline
01
Input Layer
User uploads live feed, single image, or batch video stream via modern web client.
02
API Gateway (FastAPI)
Validates media payloads, enforces size limits, and delegates video tasks to an asynchronous background worker pool.
03
Inference Engine (YOLOv8 Core)
Executes forward pass, applies Non-Maximum Suppression (NMS), and classifies 10 target classes.
04
Temporal Smoothing Filter
5-frame temporal buffer prevents transient false alarms caused by temporary occlusions.
05
Persistence & Analytics Store
Writes incident frames, bounding box coordinates, and session analytics to local JSON datastore.
06
Presentation Layer
Delivers real-time annotated visual overlays, live safety metrics, and alert triggers.

## Slide 8
Tools & Technologies Stack
End-to-End Modern Software & ML Stack
Machine Learning & Vision
YOLOv8 (Ultralytics)
PyTorch
ONNX Runtime (Opset 17 export for edge acceleration)
OpenCV
NumPy
Backend & Service Layer
FastAPI (Python 3.10+ high-performance asynchronous REST API)
Uvicorn (ASGI server implementation)
Pydantic (data validation and settings management)
BackgroundTasks (non-blocking asynchronous video decoding and processing)
Frontend & User Interface
React 18 with TypeScript
Vite 5 (high-speed build tool and development server)
Tailwind CSS 3.4 (utility-first responsive styling)
Radix UI & shadcn/ui (accessible UI component primitives)
Framer Motion (interactive micro-animations and dashboard transitions)
Lucide React (vector iconography)

## Slide 9
Expected Outputs & Application Deliverables
Comprehensive Safety Monitoring & Incident Analytics
Visual Detections
Real-time bounding box annotations with distinct colour-coding (Green for Compliance, Red for Violations, Cyan for Site Context).
Interactive Safety Dashboard
Real-time Site Safety Compliance Score (percentage of compliant vs total workers). Detection Metrics: Live mAP indicator, active alert frequency, and processed frame rates.
Automated Incident Logging
Immediate snapshot capture of violation events. Timestamped tabular log with worker identifier, violation category, and confidence score.
Operational Control & Customisation
Dynamic confidence threshold (0.1 to 0.95) and NMS IoU adjustment from the UI. Model weight hot-reloading capability for rapid updates without server restarts.

## Slide 10
Summary, Progress Status & Future Roadmap
Review #1 Milestones & Next Phase Execution
Milestones Completed (Review #1)
Curation and preprocessing of 2,801 construction safety images across 10 classes.
Full training and evaluation of YOLOv8m model achieving 88.07% mAP@0.5.
Implementation of FastAPI asynchronous backend and React TypeScript UI dashboard.
End-to-end integration of single image and multi-frame video inference pipelines.
Next Steps (Review #2 & Beyond)
Integration of real-time RTSP camera streaming protocols.
Multi-camera zone management and automated alert notifications (SMS/Email/WebSockets).
Model quantisation (INT8 / TensorRT) for deployment on edge devices like NVIDIA Jetson.